## Slide 1
HyGenICC:
Hypervisor-based Generic IP Congestion Control for Virtualized Data Centers
Conference Paper in Proceedings of ICC16 By
Ahmed M. Abdelmoniem, Brahim Bensaou, Amuda James Abu
Presented By
Ahmed M. Abdelmoniem
The Hong Kong University of Science and Technology

## Slide 2: Congestion in Data Centers
ToR
switches
Aggregation
switches
core routers
Servers
pod
1000s of servers connected by commodity switches.
Variety of traffics and application requirements (i.e, High throughput vs Low Latency)
Tenants are free to choose their transport protocol.

## Slide 3: Congestion in Data Centers
switch
shared buffer
links
DCTCP
flows
TCP
flow
Different TCP flavours are not friendly to each other.
Introduction of new transport protocols like DCTCP…
Use of UDP instead of TCP (e.g., Facebook memcache).
UDP
flow

## Slide 4: Inter-Protocol Unfairness
Impact of different congestion-responsive transport protocol coexistent  unfair bandwidth sharing [1]
TCP
flows
router
Shared Buffer
link
packets
in buffer
DCTCP or UDP
flows

## Slide 5: NS2 simulation
A scenario where a tagged TCP flow competes against either same TCP flavor, DCTCP or UDP
Tagged TCP flow starts at 5th second and continues until 15.
The competing flow starts at 0th second and stops at 10.

## Slide 6: Does ECN marking help?
ECN marking allows faster response to congestion.
Improves TCP’s performance and smoothens variations.
But is that enough? Still unfair?

## Slide 7: Recent congestion control schemes
DCTCP [Alizadeh 2010]
  limits delays by refined ECN scheme to smooth rate variations
D3 [Wilson 2011]
  “deadline driven delivery”
D2TCP [Vamanan 2012]
  combines aspects of previous two
PDQ [Hong 2012]
  size-based pre-emptive scheduling
Evaluations assume all data center flows implement the same recommended protocol and/or application’s (VMs) cooperation

## Slide 8: Efficient Solution Requirements
Independent of the transport protocol.
Allows the coexistence of different protocols.
Fits with all TCP/UDP flavors.
No modifications to the VM’s network stack.
Simple enough for easy deployment
Point to Network layer congestion control, but …
The challenge is to achieve all of these Conflicting Requirements.

## Slide 9: HyGenICC IP Congestion Control
IP congestion control would avoid drawbacks of previous work
ECN is an efficient mechanism for congestion indication
End-host hypervisor regulates the sending rates of the VMs
Sender
NIC
Hypervisor
VM1
VM2
Receiver
NIC
Hypervisor
VM3
VM4
DCN
10
ECT
11
CE
1
IPR
1
IPR
R2
R1
Flow Table

## Slide 10: Two Key Ideas
Sender monitors congestion feedback and manage per-VM rate limiters.
  If congestion feedback received  adjust rate limiters.
  HyGenICC is located at the exit point of all VMs (i.e, hypervisor or NIC or between).
Receiver intercepts ECN info (CE) and relays back to senders.
  Keep track of a counter of ECN marks per S-D VMs.
  Set “IPR-bit” as a feedback of ECN on returning packets.
  Send explicit feedback packet if necessary.
Operations Can be offloaded to the NIC.
ECN functionality available in most commodity switches.

## Slide 11: Does HyGenICC work?
Rate limiting can ensure fair bandwidth sharing.
Adapting rate limiters to the extent of the congestion.
But is that enough? Fairness + Work-Conservation is achieved.

## Slide 12: ECN Responsive VMs
VMs react to congestion as well  smoother and faster response.
Tenants can manage ECN markings in their overlay networks.

## Slide 13: HyGenICC with more senders
Number of sources are increased to 7 competing against TCP.
Converges to the fair-share with full link utilization .
But is it converging fast? <1 sec convergence is not bad for long-lived flows lasting 10-100s of seconds

## Slide 14: Why HyGenICC Works
Network Layer Solution
  Relies on network layer functions→ transport independent.
  Short control loop→ sources react fasters.
Fits all transport protocols
  IP based approach→ relying on ECN notifications.
3. Simple enough for deployment
  Modifies the hypervisor (or NIC)→ immediate batch to end-host.
  Requires function available in commodity switch → no upfront deployment costs.

## Slide 15: Thanks – Questions are welcomed
For Further Questions or feedback, kindly reach me at
amas@cse.ust.hk

## Slide 16: References
[Irteza 2014] Irteza, S. M., Ahmed, A., Farrukh, S., Memon, B. N., & Qazi, I. A. (2014). On the coexistence of transport protocols in data centers. In 2014 IEEE International Conference on Communications (ICC) (pp. 3203–3208)
[Alizadeh 2010] M. Alizadeh, A. Greenberg, D. A. Maltz, J. Padhye, P. Patel, B. Prabhakar, S. Sengupta, and M. Sridharan, “Data center TCP (DCTCP),” ACM SIGCOMM Computer Communication Review, vol. 40, p. 63, 2010.
[Wilson 2011] Wilson, C., Ballani, H., Karagiannis, T., & Rowstron, A. (2011). Better Never than Late: Meeting Deadlines in Datacenter Networks. In Proc. ACM Conference on Communications Architectures, Protocols and Applications (SIGCOMM’11).
[Vamanan 2012] Vamanan, B., Hasan, J., & Vijaykumar, T. N. (2012). Deadline-aware datacenter tcp (D2TCP). ACM SIGCOMM Computer Communication
[Hong 2012] Hong, C.-Y., Caesar, M., & Godfrey, P. B. (2012). Finishing flows quickly with preemptive scheduling. In Proceedings of the ACM SIGCOMM 2012 conference on Applications, technologies, architectures, and protocols for computer communication - SIGCOMM ’12 (p. 127).

## Slide 17: Intra-Protocol Fairness
Same protocols are fair to each other
router
Shared Buffer
link
packets
in buffer
TCP
flow
TCP
flow

## Slide 18: Intra-Protocol Unfairness
Impact of large and small flow coexistence: unfair bandwidth sharing
TCP
flow
router
Shared Buffer
link
packets
in buffer
Mice
flow

## Slide 19: Inter-Protocol Unfairness
Impact of congestion-unresponsive transport protocol coexistent  unfair bandwidth sharing
TCP
flow
router
Shared Buffer
link
packets
in buffer
“UDP”
flow
UDP
TCP

## Slide 20: Does Static (Centralized) rate allocation help?
Rate limiting can ensure fair bandwidth sharing.
Improves fairness regardless of the transport protocol.
But is that enough? Work-conservation (utilization)?
Aggregate
Tagged

## Slide 21: Advantages of Network Congestion Control
Fairness is imposed at network layer
  Flows use the congestion control they want (e.g, TCP cubic, reno, DCTCP, UDP, …etc)
  No danger from “unresponsive flows”
Realizes implicit service differentiation
  Since rate of streaming flows generally less than fair rate
  Increase the number of allowable flows in network
Network
Congestion
Control
fair rate

## Slide 22: HyGenICC: How sender works?
The sending VMs using any transport protocol would send at their nominal rate to the hypervisor.
The hypervisor runs a simple counting Token-Bucket Rate (TBR) limiters to cap VMs rates to their fair-share of their physical NIC capacity.
The hypervisor monitors any incoming “IPR-bit” flags or feed-back messages from the receiving end-hosts.
TBRs are adaptively adjusted to account for the amount of congestion each source is causing in the network
Notes: - All packets of any transport protocol is ECN-Capable marked to not be dropped at the queues over the path.

## Slide 23: HyGenICC: How receiver works?
The receiving end-hosts monitors incoming ECN marks on data packets.
The hypervisor clears the marks and account it for the sending host in the table.
After ACK is ready to transmitted the hypervisor marks the “IPR-bit”
If no ACK is sent after waiting for a period of time the hypervisors sends explicit feed-back message.

## Slide 24: Conclusions
HyGenICC satisfies all mentioned requirements for Data Center congestion control.
  Independent of transport protocol or VM network stack.
  Allows the coexistence of different protocols.
  Fits with any Protocol flavor running on any OS.
  No Modifications to Guest VMs networking stack.
Features:
  Very simple change to end-host hypervisor logic.
  Allows immediate and incremental deployment.